## Slide 1: CS 334 / CS 534 Networking
Lecture 05
The Physical Layer

## Slide 2: Physical Layer
Function
  Get bits across a physical medium
Key challenge
  How to represent bits in analog
  Ideally, want high bit rate
  But, must avoid descynchronization
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3
We have two discrete signals, high and low, to encode 1 and 0
Transmission is synchronous. I.e., there is a clock that controls signal sampling
Amplitude and duration of signal must be significant
Time
Sample

## Slide 4: Non-Return to Zero (NRZ)
1  High signal, 0  Low signal
Problem: long strings of 0 or 1 cause desynchronizationI
  How to distinguish lots of 0s from no signal at all?!
  How to recover the clock during lots of 1s?
Clock
NRZ
0
0
0
0
0
0
1
1
1
1

## Slide 5: Desynchronization
Problem: How to recover the clock during sequences of 1s or 0s?!
NRZ
0
0
1
1
1
1
1
1
1
1
Transitions signify clock ticks
0
0
1
1
1
1
1
1
1
Receiver misses a 1 due to skew

## Slide 6: Non-Return to Zero Inverted (NRZI)
1  make transition, 0  remain the same
Solves the problem for sequences of 1s, but not 0s
Clock
NRZI
0
0
0
0
0
0
1
1
1
1

## Slide 7: 4-bit/5-bit (100 Mbps Ethernet)
Observations: NRZI works as long as no sequences of 0
Idea: encode all 4-bit sequences as 5-bit sequences with no more than one leading 0 and two trailing 0s
0000 11110
0001 01001
0010 10100
0011 10101
0100 01010
0101 01011
0110 01110
0111 01111
1000 10010
1001 10011
1010 10110
1011 10111
1100 11010
1101 11011
1110 11100
1111 11101
4-bit 5-bit
4-bit 5-bit

## Slide 8: 4-bit/5-bit (100 Mbps Ethernet)
Observations: NRZI works as long as no sequences of 0
Idea: encode all 4-bit sequences as 5-bit sequences with no more than one leading 0 and two trailing 0s
0000 11110
0001 01001
0010 10100
0011 10101
0100 01010
0101 01011
0110 01110
0111 01111
1000 10010
1001 10011
1010 10110
1011 10111
1100 11010
1101 11011
1110 11100
1111 11101
4-bit 5-bit
4-bit 5-bit
Tradeoff:
Efficiency drops to 80%

## Slide 9: 4-bit/5-bit (100 Mbps Ethernet)
Observations: NRZI works as long as no sequences of 0
Idea: encode all 4-bit sequences as 5-bit sequences with no more than one leading 0 and two trailing 0s
0000 11110
0001 01001
0010 10100
0011 10101
0100 01010
0101 01011
0110 01110
0111 01111
1000 10010
1001 10011
1010 10110
1011 10111
1100 11010
1101 11011
1110 11100
1111 11101
4-bit 5-bit
4-bit 5-bit
Tradeoff:
Efficiency drops to 80%
8-bit / 10-bit used in Gigabit Ethernet

## Slide 10: Manchester
1  High-to-low, 0  low-to-high
Good: Solves clock skew (every bit is a transition)
Bad: Halves throughput (two clock cycles per bit)
Clock
NRZI
0
0
0
1
1