## Slide 1: CS 334 / CS 534 Networking
Lecture 06
Data Link

## Slide 2: Data Link Layer
Function
  Send blocks of data (frames) between physical devices
  Regulate access to the physical media
Key Challenges:
  How to delineate frames?
  How to detect errors?
  How to perform media access control (MAC)?
  How to recover from and avoid collisions?
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Framing
Physical layer determines how bits are encoded
Next step, how to encode blocks of data?
  Packet switched networks
  Each packet includes routing information
  Data boundaries must be known so headers can be read
Types of framing
  Byte oriented protocols
  Bit oriented protocols
  Clock based protocols

## Slide 4: Byte Oriented: Sentinel Approach
Add START and END sentinels to the data
Problem: what if END appear in the data?
  Add a special DLE (Data Link Escape) character before END
  What if DLE appears in the data? Add DLE before it.
  Similar to escape sequences in C
    printf(“You must \”escape\” quotes in strings”);
    printf(“You must \\escape\\ forward slashes as well”);
Used by Point-to-Point protocol, e.g. modem, DSL, cellular
Data
START
END
END
DLE
DLE
DLE
Notes: https://en.wikipedia.org/wiki/Binary_Synchronous_Communications examples of Special Patterns

## Slide 5: Byte Oriented: Byte Counting
Sender: insert length of the data in bytes at the beginning of each frame
Receiver: extract the length and read that many bytes
Data
132

## Slide 6: Bit Oriented: Bit Stuffing
Add sentinels to the start and end of data
  Both sentinels are the same
  Example: 01111110 in High-level Data Link Protocol (HDLC)
Sender: insert a 0 after each 11111 in data
  Known as “bit stuffing”
Receiver: after seeing 11111 in the data…
  111110  remove the 0 (it was stuffed)
  111111  look at one more bit
    1111110  end of frame
    1111111  error! Discard the frame
Disadvantage: 20% overhead at worst
Data
01111110
01111110
Notes: Sender adds a 0 after 5 1 bits. If the sender doesn’t do this, and 6 1s are in the payload followed by a 0, the receiver will read the data stream as an end flag. If there are 6 1s in the payload followed by a 1, the receiver will discard the frame. IT WILL ALWAYS STUFF. 20% at worst because after every 5th bit a 0 will be stuffed. 1/5 = 20%
Computer knows to throw away stuffed bit, it reads data like it wasn’t there, just knows not to terminate.

## Slide 7: Clock-based Framing: SONET
Synchronous Optical Network
  Transmission over very fast optical links
  STS-n, e.g. STS-1: 51.84 Mbps, STS-768: 36.7 Gbps
STS-1 frames based on fixed sized frames
  9*90 = 810 bytes
Physical layer details
  Bits are encoded using NRZ
  Payload is XORed with a special 127-bit pattern to avoid long sequences of 0 and 1
90 Columns
9 Rows
Payload
Overhead
Special start pattern
Notes: STS – Synchronous Transport Signal.

## Slide 8: Dealing with Noise
The physical world is inherently noisy
  Interference from electrical cables
  Cross-talk from radio transmissions, microwave ovens
  Solar storms
How to detect bit-errors in transmission?
How to recover from errors?

## Slide 9: Naïve Error Detection
Idea: send two copies of each frame
  if (memcmp(frame1, frame2) != 0) { OH NOES! ERROR!!!! }
Why is this a bad idea?
  Extremely high overhead
  Poor protection against errors
    Twice the data means twice the chance for bit errors
Notes: MEMCMP – Memory Compare

## Slide 10: Naïve Error Detection
Idea: send two copies of each frame
  if (memcmp(frame1, frame2) != 0) { OH NOES! ERROR!!!! }
Why is this a bad idea?
  Extremely high overhead
  Poor protection against errors
    Twice the data means twice the chance for bit errors

## Slide 11: Naïve Error Detection
Idea: send two copies of each frame
  if (memcmp(frame1, frame2) != 0) { OH NOES! ERROR!!!! }
Why is this a bad idea?
  Extremely high overhead
  Poor protection against errors
    Twice the data means twice the chance for bit errors

## Slide 12: Naïve Error Detection
Idea: send two copies of each frame
  if (memcmp(frame1, frame2) != 0) { OH NOES! ERROR!!!! }
Why is this a bad idea?
  Extremely high overhead
  Poor protection against errors
    Twice the data means twice the chance for bit errors

## Slide 13: Naïve Error Detection
Idea: send two copies of each frame
  if (memcmp(frame1, frame2) != 0) { OH NOES! ERROR!!!! }
Why is this a bad idea?
  Extremely high overhead
  Poor protection against errors
    Twice the data means twice the chance for bit errors

## Slide 14: Parity Bits
Detects 1-bit errors
Not reliable against bursty errors
Idea: add extra bits to keep the number of 1s even
  Example: 7-bit ASCII characters + 1 parity bit
0101001
1
0
1
1
1
1011110
0110100
1101001
0001110
Notes: Just makes the number of 1s even.
Failed Transmission Scenario – Alice sends 1001 parity bit 0 => 10010 … some transmission error … bob receives 11010 which is 1101 parity bit0 – Bob reports incorrect transmission
Burst Error – Multiple bits changed. The length of burst error is measured from first changed bit to last changed bit

## Slide 15: Two Dimensional Parity
Can detect all 1-, 2-, and 3-bit errors, some 4-bit errors
14% overhead
0101001
1101001
1011110
0001110
0110100
1011111
1
0
1
1
1
0
1111011
0
Parity bit for each row
Parity bit for each column
Parity bit for the parity byte

## Slide 16: Two Dimensional Parity Examples
0101001
1101001
1011110
0001110
0110100
1011111
1
0
1
1
1
0
1111011
0
Odd number of 1s
Odd Number of 1s
1
1
Odd number of 1s
1
Odd number of 1s
0

## Slide 17: Checksums
Idea:
  Add up the bytes in the data
  Include the sum in the frame
Use ones-complement arithmetic
Lower overhead than parity: 16 bits per frame
But, not resilient to errors
Used in UDP, TCP, and IP
Data
START
END
Checksum
0101001
1101001= 10010010
+
0
1
Notes: What is this called? Why is that important? Collisions. SHA 1 first collision took 2 years and 9 quintillion computations

## Slide 18: Cyclic Redundancy Check (CRC)
Uses field theory to compute a semi-unique value for a given message
Much better performance than previous approaches
  Fixed size overhead per frame (usually 32-bits)
  Quick to implement in hardware
  Only 1 in 2^32 chance of missing an error with 32-bit CRC
Details are going to be in the book/Wikipedia
  Seriously, just google it and you should be fine 
Notes: 1 in a 4,294,967,296‬ -- 4.2 Trillion

## Slide 19: What About Reliability?
How does a sender know that a frame was received?
  What if it has errors?
  What if it never arrives at all?!?
Sender
Receiver
Time
Frame
ACK
Acknowledgement

## Slide 20: Stop and Wait
Simplest form of reliability
Example: Bluetooth
Problems?
  Utilization
  Can only have one frame in flight at any time
10Gbps link and 10ms delay
  Need 100 Mbit to fill the pipe
  Assume packets are 1500B
1500B*8bit/(2*10ms) = 600Kbps
Utilization is 0.006%
Sender
Receiver
Frame
ACK
Timeout
Frame
Timeout
Frame

## Slide 21: Sliding Window
Allow multiple outstanding, un-ACKed frames
Number of un-ACKed frames is called the window
Sender
Receiver
Frames
ACKs
Window
Made famous by TCP
  We’ll look at this in more detail later

## Slide 22: Should We Error Check in the Data Link?
Recall the End-to-End Argument
Cons:
  Error free transmission cannot be guaranteed
  Not all applications want this functionality
  Error checking adds CPU and packet size overhead
  Error recovery requires buffering
Pros:
  Potentially better performance than app-level error checking
Data link error checking in practice
  Most useful over lossy links
  Wifi, cellular, satellite
Notes: Simplify(lossy) = Dissipation of Energy

## Slide 23: Next Class
We will finish our discussion of Data Link layer