## Slide 1: CS 334 / CS 534 Networking
Lecture 07
Bridging

## Slide 2: Just Above the Data Link Layer
Bridging
  How do we connect LANs?
Function:
  Route packets between LANs
Key challenges:
  Plug-and-play, self configuration
  How to resolve loops
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Recap
Originally, Ethernet was a broadcast technology
Pros: Simplicity
  Hardware is dumb and cheap
Cons: No scalability
  More hosts = more collisions
Tee Connector
Terminator
Hub
Repeater

## Slide 4: The Case for Bridging
Need a device that can bridge different LANs
  Only forward packets to intended recipients
  No broadcast!
Hub
A
C
B
A
C
B
Send Packet
B  C
Send Packet
B  C
Bridge

## Slide 5: Bridging the LANs
Bridging limits the size of collision domains
  Vastly improves scalability
  Question: could the whole Internet be one bridging domain?
Tradeoff: bridges are more complex than hubs
  Physical layer device vs. data link layer device
  Need memory buffers, packet processing hardware, routing tables
Hub
Hub

## Slide 6: Bridge Internals
Bridges have memory buffers to queue packets
Bridge is intelligent, only forwards packets to the correct output
Bridges are high performance, full N x line rate is possible
Switch Fabric
Inputs
Outputs
Bridge
Makes routing decisions
Hub
Memory buffer

## Slide 7: Bridges
Original form of Ethernet switch
Connect multiple IEEE 802 LANs at layer 2 (Data Link)
Goals
  Reduce the collision domain
  Complete transparency
    Plug-and-play, self configuring
    No hardware or software changes on hosts/hubs
    Should not impact existing LAN operations
Hub

## Slide 8: Bridges
Original form of Ethernet switch
Connect multiple IEEE 802 LANs at layer 2 (Data Link)
Goals
  Reduce the collision domain
  Complete transparency
    Plug-and-play, self configuring
    No hardware or software changes on hosts/hubs
    Should not impact existing LAN operations
Hub
Forwarding of frames
Learning of (MAC) addresses
Spanning Tree Algorithm (to handle loops)

## Slide 9: Frame Forwarding Tables
Each bridge maintains a forwarding table
00:00:00:00:00:DD | 1 | 3 minutes
MAC Address | Port | Age
00:00:00:00:00:AA | 1 | 1 minute
00:00:00:00:00:BB | 2 | 7 minutes
00:00:00:00:00:CC | 3 | 2 seconds

## Slide 10: Frame Forwarding in Action
Assume a frame arrives on port 1
If the destination MAC address is in the forwarding table, send the frame on the correct output port
If the destination MAC isn’t in the forwarding table, broadcast the frame on all ports except port 1
  Don’t send the frame back out on the port it came in on 

## Slide 11: Frame Forwarding in Action
Assume a frame arrives on port 1
If the destination MAC address is in the forwarding table, send the frame on the correct output port
If the destination MAC isn’t in the forwarding table, broadcast the frame on all ports except port 1
  Don’t send the frame back out on the port it came in on 

## Slide 12: Frame Forwarding in Action
Assume a frame arrives on port 1
If the destination MAC address is in the forwarding table, send the frame on the correct output port
If the destination MAC isn’t in the forwarding table, broadcast the frame on all ports except port 1
  Don’t send the frame back out on the port it came in on 

## Slide 13: Frame Forwarding in Action
Assume a frame arrives on port 1
If the destination MAC address is in the forwarding table, send the frame on the correct output port
If the destination MAC isn’t in the forwarding table, broadcast the frame on all ports except port 1
  Don’t send the frame back out on the port it came in on 

## Slide 14: Frame Forwarding in Action
Assume a frame arrives on port 1
If the destination MAC address is in the forwarding table, send the frame on the correct output port
If the destination MAC isn’t in the forwarding table, broadcast the frame on all ports except port 1
  Don’t send the frame back out on the port it came in on 
Port 1
Port 3
Port 2
Port 4

## Slide 15: Learning Addresses
Manual configuration is possible, but…
  Time consuming
  Error prone
  Not adaptable (hosts may get added or removed)
Instead, learn addresses using a simple heuristic
  Look at the source of frames that arrive on each port!

## Slide 16: Learning Addresses
Manual configuration is possible, but…
  Time consuming
  Error prone
  Not adaptable (hosts may get added or removed)
Instead, learn addresses using a simple heuristic
  Look at the source of frames that arrive on each port!

## Slide 17: Learning Addresses
Manual configuration is possible, but…
  Time consuming
  Error prone
  Not adaptable (hosts may get added or removed)
Instead, learn addresses using a simple heuristic
  Look at the source of frames that arrive on each port!

## Slide 18: Learning Addresses
Manual configuration is possible, but…
  Time consuming
  Error prone
  Not adaptable (hosts may get added or removed)
Instead, learn addresses using a simple heuristic
  Look at the source of frames that arrive on each port!

## Slide 19: Learning Addresses
Manual configuration is possible, but…
  Time consuming
  Error prone
  Not adaptable (hosts may get added or removed)
Instead, learn addresses using a simple heuristic
  Look at the source of frames that arrive on each port!

## Slide 20: Learning Addresses
Manual configuration is possible, but…
  Time consuming
  Error prone
  Not adaptable (hosts may get added or removed)
Instead, learn addresses using a simple heuristic
  Look at the source of frames that arrive on each port!

## Slide 21: Learning Addresses
Manual configuration is possible, but…
  Time consuming
  Error prone
  Not adaptable (hosts may get added or removed)
Instead, learn addresses using a simple heuristic
  Look at the source of frames that arrive on each port!
Hub
00:00:00:00:00:AA
00:00:00:00:00:BB
Port 1
Port 2
00:00:00:00:00:BB | 2 | 0 minutes
MAC Address | Port | Age
00:00:00:00:00:AA | 1 | 0 minutes
Delete old entries after a timeout

## Slide 22: Complicated Learning Example
<Src=AA, Dest=FF>
<Src=CC, Dest=AA>
<Src=EE, Dest=CC>
FF
EE
DD
CC
BB
AA
Port 1
Port 2
Port 1
Port 2
Hub
Hub
Hub
AA | 1
AA | 1
CC | 2
CC | 1
EE | 2
EE | 2
Bridge 1
Bridge 2

## Slide 23: The Danger of Loops
<Src=AA, Dest=DD>
This continues to infinity
  How do we stop this?
Remove loops from the topology
  Without physically unplugging cables
802.1 uses an algorithm to build and maintain a spanning tree for routing
AA
Port 1
Hub
Port 1
Hub
Port 2
Port 2
AA | 1
AA | 1
BB
CC
DD
AA | 2
AA | 2
AA | 1
AA | 1
Notes: Remeber, if there is no entry in a bridge for a given source, it will update the port table accordingly.
If the entry in the table does not exist, broadcast on all other ports. Which then updates the other bridge, showing it coming in from port 2.

## Slide 24: Spanning Tree Definition
A subset of edges in a graph that:
  Span all nodes
  Do not create any cycles
This structure is a tree
1
4
2
5
6
3
7
1
4
2
5
6
3
7
5
1
4
2
6
3
7

## Slide 25: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Calculate shortest paths
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 26: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Calculate shortest paths
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 27: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Calculate shortest paths
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 28: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Calculate shortest paths
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 29: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Calculate shortest paths
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 30: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Calculate shortest paths
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 31: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Calculate shortest paths
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 32: 802.1 Spanning Tree Approach
Elect a bridge to be the root of the tree
Every bridge finds shortest path to the root
Union of these paths becomes the spanning tree
Bridges exchange Configuration Bridge Protocol Data Units (BPDUs) to build the tree
  Used to elect the root bridge
  Calculate shortest paths
  Locate the next hop closest to the root, and its port
  Select ports to be included in the spanning trees

## Slide 33: Definitions (KNOW THESE)
Bridge ID (BID) = <Random Number>
Root Bridges: bridge with the lowest BID in the tree
Path Cost: cost (in hops) from a transmitting bridge to the root
Each port on a bridge has a unique Port ID
Root Port: port that forwards to the root on each bridge
Designated Bridges: the bridge on a LAN that provides the minimal cost path to the root
  The designated bridge on each LAN is unique

## Slide 34: Definitions (KNOW THESE)
Bridge ID (BID) = <Random Number>
Root Bridges: bridge with the lowest BID in the tree
Path Cost: cost (in hops) from a transmitting bridge to the root
Each port on a bridge has a unique Port ID
Root Port: port that forwards to the root on each bridge
Designated Bridges: the bridge on a LAN that provides the minimal cost path to the root
  The designated bridge on each LAN is unique

## Slide 35: Definitions (KNOW THESE)
Bridge ID (BID) = <Random Number>
Root Bridges: bridge with the lowest BID in the tree
Path Cost: cost (in hops) from a transmitting bridge to the root
Each port on a bridge has a unique Port ID
Root Port: port that forwards to the root on each bridge
Designated Bridges: the bridge on a LAN that provides the minimal cost path to the root
  The designated bridge on each LAN is unique

## Slide 36: Definitions (KNOW THESE)
Bridge ID (BID) = <Random Number>
Root Bridges: bridge with the lowest BID in the tree
Path Cost: cost (in hops) from a transmitting bridge to the root
Each port on a bridge has a unique Port ID
Root Port: port that forwards to the root on each bridge
Designated Bridges: the bridge on a LAN that provides the minimal cost path to the root
  The designated bridge on each LAN is unique

## Slide 37: Definitions (KNOW THESE)
Bridge ID (BID) = <Random Number>
Root Bridges: bridge with the lowest BID in the tree
Path Cost: cost (in hops) from a transmitting bridge to the root
Each port on a bridge has a unique Port ID
Root Port: port that forwards to the root on each bridge
Designated Bridges: the bridge on a LAN that provides the minimal cost path to the root
  The designated bridge on each LAN is unique

## Slide 38: Definitions (KNOW THESE)
Bridge ID (BID) = <Random Number>
Root Bridges: bridge with the lowest BID in the tree
Path Cost: cost (in hops) from a transmitting bridge to the root
Each port on a bridge has a unique Port ID
Root Port: port that forwards to the root on each bridge
Designated Bridges: the bridge on a LAN that provides the minimal cost path to the root
  The designated bridge on each LAN is unique

## Slide 39: Definitions (KNOW THESE)
Bridge ID (BID) = <Random Number>
Root Bridges: bridge with the lowest BID in the tree
Path Cost: cost (in hops) from a transmitting bridge to the root
Each port on a bridge has a unique Port ID
Root Port: port that forwards to the root on each bridge
Designated Bridges: the bridge on a LAN that provides the minimal cost path to the root
  The designated bridge on each LAN is unique

## Slide 40: Determining the Root
Initially, all hosts assume they are the root
Bridges broadcast BDUs:
Based on received BDUs, each switch chooses:
  A new root (smallest known Root ID)
  A new root port (what interface goes towards the root)
  A new designated bridge (who is the next hop to the root)

## Slide 41: Determining the Root
Initially, all hosts assume they are the root
Bridges broadcast BDUs:
Based on received BDUs, each switch chooses:
  A new root (smallest known Root ID)
  A new root port (what interface goes towards the root)
  A new designated bridge (who is the next hop to the root)
Root ID
Path Cost to Root
Bridge ID
Notes: BDU -- Bridge Data Unit

## Slide 42: Determining the Root
Initially, all hosts assume they are the root
Bridges broadcast BDUs:
Based on received BDUs, each switch chooses:
  A new root (smallest known Root ID)
  A new root port (what interface goes towards the root)
  A new designated bridge (who is the next hop to the root)
Root ID
Path Cost to Root
Bridge ID

## Slide 43: Determining the Root
Initially, all hosts assume they are the root
Bridges broadcast BDUs:
Based on received BDUs, each switch chooses:
  A new root (smallest known Root ID)
  A new root port (what interface goes towards the root)
  A new designated bridge (who is the next hop to the root)
Root ID
Path Cost to Root
Bridge ID

## Slide 44: Determining the Root
Initially, all hosts assume they are the root
Bridges broadcast BDUs:
Based on received BDUs, each switch chooses:
  A new root (smallest known Root ID)
  A new root port (what interface goes towards the root)
  A new designated bridge (who is the next hop to the root)
Root ID
Path Cost to Root
Bridge ID

## Slide 45: Determining the Root
Initially, all hosts assume they are the root
Bridges broadcast BDUs:
Based on received BDUs, each switch chooses:
  A new root (smallest known Root ID)
  A new root port (what interface goes towards the root)
  A new designated bridge (who is the next hop to the root)
Root ID
Path Cost to Root
Bridge ID

## Slide 46: Comparing BPDUs
if R1 < R2: use BPDU1
else if R1 == R2 and Cost1 < Cost2: use BPDU1
else if R1 == R2 and Cost1 == Cost 2 and B1 < B2:
use BPDU1
else: use BPDU2
R1
Cost1
B1
R2
Cost2
B2
BPDU1
BPDU2

## Slide 47: Bridges vs Switches
Bridges make it possible to increase LAN capacity
  Reduces the amount of broadcast packets
  No loops
Switch is a special case of a bridge
  Each port is connected to a single host
    Either a client machine
    Or another switch
  Links are full duplex
  Simplified hardware: no need for CSMA/CD!
  Can have different speeds on each port

## Slide 48: Switching the Internet
Capabilities of switches:
  Network-wide routing based on MAC addresses
  Learn routes to new hosts automatically
  Resolve loops
Could the whole Internet be one switching domain?
NO

## Slide 49: Limitations of MAC Routing
Inefficient
  Flooding packets to locate unknown hosts
Poor Performance
  Spanning tree does not balance load
  Hot spots
Extremely Poor Scalability
  Every switch needs every MAC address on the Internet in its routing table!
  IP addresses these problems