## Slide 1: CS 334 / CS 534 Networking
Lecture 08.1
Network

## Slide 2: Network Layer
Function:
  Route packets end-to-end on a network, through multiple hops
Key challenge:
  How to represent addresses
  How to route packets
    Scalability
    Convergence
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 3: Routers, revisited
How to connect multiple LANs?
LANs may be incompatible
  Ethernet, WiFi, etc…
Connected networks for an internetwork
  The Internet is the best known example
Routers

## Slide 4: Structure of the Internet
Ad-hoc interconnection of networks
  No organized topology
  Vastly different technologies, link capacities
Packets travel end-to-end by hopping through networks
  Routers “peer” (connect) different networks
  Different packets may take different routes
Network 2
Network 1
Network 3
Network 4

## Slide 5: Internetworking Issues
Naming / Addressing
  How do you designate hosts?
Routing
  Must be scalable (i.e. a switched Internet won’t work)
Service Model
  What gets sent?
  How fast will it go?
  What happens if there are failures?
  Must deal with heterogeneity
    Remember, every network is different
Internet Service Model
Best-effort (i.e. things may break)
Store-and-forward datagram network
Lowest common denominator

## Slide 6: Possible Addressing Schemes
Flat
  e.g. each host is identified by a 48-bit MAC address
  Router needs an entry for every host in the world
    Too big
    Too hard to maintain (hosts come and go all the time)
Hierarchy
  Addresses broken down into segments
  Each segment has a different level of specificity

## Slide 7: Example: Telephone Numbers
1-205-934-2197
Campbell Hall
Room 132
Very General
Very Specific
Campbell Hall
Rom 141
5473
Updates are Local

## Slide 8: Binary Hierarchy Example
1**
10*
11*
100
101
110
111
0**
00*
01*
000
001
010
011
Datagram, Destination = 101

## Slide 9: IP Addressing
IPv4: 32-bit addresses
  Usually written in dotted notation, e.g. 192.168.21.76
  Each number is a byte
  Stored in Big Endian order
11000000
C0
192
10101000
A8
168
00010101
15
21
01001100
4C
76
Decimal
Hex
Binary
0
8
16
24
31

## Slide 10: IP Addressing and Forwarding
Routing Table Requirements
  For every possible IP, give the next hop
  But for 32-bit addresses, 232 possibilities!
Hierarchical address scheme
  Separate the address into a network and a host
Host
Network
Pfx
0
31
Known by all routers
Known by edge (LAN) routers
Notes: Prefix – Essentially what you are assignened

## Slide 11: Classes of IP Addresses
Class A
Host
Ntwk
0
0
31
1
8
Example: MIT
18.*.*.*
1-126
Class B
Host
Network
10
0
31
2
16
Example: UAB
138.26.*.*
128-191
8
Class C
Host
Network
110
0
31
3
24
Example:
216.63.78.*
192-223
8
16
16
24
24

## Slide 12: How Do You Get Ips?
IP address ranges controlled by IANA
  Internet Assigned Numbers Authority
  Roots go back to 1972, ARPANET, UCLA
  Today, part of ICANN
IANA may grant you a class of IPs
  You may then begin installing routers that advertise routes to your new IP range

## Slide 13: Two Level Hierarchy
…
…
Host
Network
Pfx
Subtree size determined by network class

## Slide 14: Class Sizes
Class | Prefix Bits | Network Bits | Number of Classes | Hosts per Class
A | 1 | 7 | 27 – 2 = 126 (0 and 127 are reserved) | 224 – 2 = 16,777,214 (All 0 and all 1 are reserved)
B | 2 | 14 | 214 = 16,398 | 216 – 2 = 65,534 (All 0 and all 1 are reserved)
C | 3 | 21 | 221 = 2,097,512 | 28 – 2 = 254 (All 0 and all 1 are reserved)
 |  |  | Total: 2,114,036 | 
Too many network IDs
Too small to be useful
Way too big
Notes: … why minus 2? Network address and Broadcast Address
Who owns Class A Spaces? IANA (Internet Assigned Numbers Authroity), Apple, Ford, ATT
Who owns Class B Spaces? UAB Owns 2 Rents some address space out. EBSCO owns 2 We Use A LOT
ALL 0 and ALL 1 reservered (BINARY) what it is really saying is .0 and .255 of the network address is used for a broadcast

## Slide 15: Subnets
Problem: need to break up large A and B classes
Solution: add another layer to the hierarchy
  From the outside, appears to be a single network
    Only 1 entry in routing tables
  Internally, manage multiple subnetworks
    Split the address range using a subnet mask
Host
Ntwk
Pfx
Subnet
11111111 11111111 11000000 00000000
Subnet Mask:
Notes: A subnet mask is a number that defines a range of IP addresses that can be used in a network. ... A subnet mask hides, or "masks," the network part of a system's IP address and leaves only the host part as the machine identifier.

## Slide 16: Subnet Example
Extract network:
Extract host:
10110101 11011101 01010100 01110010
IP Address:
& 11111111 11111111 11000000 00000000
Subnet Mask:
10110101 11011101 01000000 00000000
Result:
10110101 11011101 01010100 01110010
IP Address:
& ~(11111111 11111111 11000000 00000000)
Subnet Mask:
00000000 00000000 00010100 01110010
Result:
Notes: Calculate Network = Bitwise AND
Calculate Host = Negation of Bitwise AND

## Slide 17: N-Level Subnet Hierarchy
…
…
Host
Network
Pfx
Subtree size determined by length of subnet mask
Subnet
…
Tree does not have a fixed depth
Increasingly specific subnet masks
Notes: Increasingly Specfic – IANA gives you a Class B, you subnet that class B into 256 Class C, you subnet each class C into ½ of a Class C. We will look at this with CIDR

## Slide 18: Example Routing Table
Address Pattern | Subnet Mask | Destination Router
0.0.0.0 | 0.0.0.0 | Router 4
18.0.0.0 | 255.0.0.0 | Router 2
128.42.0.0 | 255.255.0.0 | Router 3
128.42.128.0 | 255.255.128.0 | Router 5
128.42.222.0 | 255.255.255.0 | Router 1
Question: 128.42.222.198 matches four rows
  Which router do we forward to?
Longest prefix matching
  Use the row with the longest number of 1’s in the mask
  This is the most specific match
Notes: Significance of 0.0.0.0 – Default Route, represents ALL possible IP addresses. Careful leaving this rule. Talk about Implicit Deny. Make them remember it! It will be on a quiz.

## Slide 19: Subnetting Revisited
Question: does subnetting solve all the problems of class-based routing?
NO
Classes are still too coarse
  Class A can be subnetted, but only 126 available
  Class C is too small
  Class B is nice, but there are only 16,398 available
Routing tables are still too big
  2.1 million entries per router

## Slide 20: Classless Inter Domain Routing
CIDR, pronounced ‘cider’
Key ideas:
  Get rid of IP classes
  Use bitmasks for all levels of routing
Arbitrary split between network and host
  Specified as a bitmask or prefix length
  Example: Northeastern
    129.10.0.0 with netmask 255.255.0.0
    129.10.0.0 / 16
Notes: CIDR is basically saying how many bits (starting from left to right) are frozen

## Slide 21: Aggregation with CIDR
Original use: aggregating class C ranges
One organization given contiguous class C ranges
  Example: Microsoft, 207.46.192.* – 207.46.255.*
  Represents 26 = 64 class C ranges
  Specified as CIDR address 207.46.192.0/18
11001111
CF
207
00101110
2E
46
11xxxxxx
C0
192
xxxxxxxx
00
0
Decimal
Hex
Binary
0
8
16
24
31
18 Bits Frozen By Netmask
14 Arbitrary Bits

## Slide 22: Example CIDR Routing Table
Address | Netmask | Third Byte | Byte Range
207.46.0.0 | 19 | 000xxxxx | 0 – 31
207.46.32.0 | 19 | 001xxxxx | 32 – 63
207.46.64.0 | 19 | 010xxxxx | 64 – 95
207.46.128.0 | 18 | 10xxxxxx | 128 – 191
207.46.192.0 | 18 | 11xxxxxx | 192 – 255
Hole in the Routing Table: No coverage for 96 – 127
207.46.96.0/19
Notes: NetMask = 19 means first 19 bits ”frozen” your third byte will have 5 “unfrozen” bits 2^5 = 32 | Byte Range starts at 0, therefore, 0-31 byte range
Netmask = same as above, however, the 19th bit is ”frozen” as a 1 which equates to 32, so you will start byte range at 32.
What happens when there is no route? Drops the packet and sends ICMP to source informing source

## Slide 23: Size of CIDR Routing Tables
From www.cidr-report.org
CIDR has kept IP routing table sizes in check
  Currently ~700,000 entries for a complete IP routing table
    Was ~450,000 in 2015 or so…
  Only required by backbone routers
Notes: Simplify(Backbone router) == Integral Piece of Enterprise Network

## Slide 24: Takeaways
Hierarchical addressing is critical for scalability
  Not all routers need all information
  Limited number of routers need to know about changes
Non-uniform hierarchy useful for heterogeneous networks
  Class-based addressing is too coarse
  CIDR improves scalability and granularity
Implementation challenges
  Longest prefix matching is more difficult than schemes with no ambiguity
Notes: Literal would be better, just not more efficient

## Slide 25: Next class
We finish up the networking layer